## Slide 1: Wilmington district Reservoir operations
Michael A (Tony) Young, P.E.
Water Management Chief
Wilmington District
Date: 08 May 2019
Jordan
Scott
Falls
Philpott
Kerr

## Slide 2: Example slides

## Slide 3
Maximize congressionally authorized purposes within existing operational guidelines
Predictable responses to varying conditions
Actively inform affected stakeholders
Water Management Goals
Flood Control
Hydropower
Water Supply
Water Quality & Low Flow Augmentation
Recreation
Fish & Wildlife Enhancement

## Slide 4
Maximize congressionally authorized purposes within existing operational guidelines
Predictable responses to varying conditions
Actively inform affected stakeholders
Water Management Goals
    Specific Water Control Plans for each Project
    Flood Operations
    Drought Contingency Plans
    Deviations

## Slide 5
Maximize congressionally authorized purposes within existing operational guidelines
Predictable responses to varying conditions
Actively inform affected stakeholders
Water Management Goals
Weekly status report & call
Face-to-face meetings
Positive, routine interaction
“Door to the Corps” for many stakeholders

## Slide 6: Example slides
Controlled Flood Storage
Guide Curve (Normal Operating Level)
Sedimentation Storage
Conservation Storage
(Water Supply, Water Quality, Power)
Typical Reservoir Profile
Each storage pool tracked separately

## Slide 7: Example slides
Guide Curve (Constant)

## Slide 8: Example slides
Guide Curve (Varying)

## Slide 9: Example slides
Guide Curve (Varying)

## Slide 10
B. Everett Jordan Dam and Lake
32.6%
67.4%

## Slide 11: Example slides
W Kerr Scott

## Slide 12: Example slides
John H Kerr

## Slide 13: Flood Operations
Temporary storage of floodwaters for release at controlled, non-damaging or less-damaging rates
Releases based on water-on-the ground…not forecasts (no pre-releases)
WCP establishes release protocols (control pts, stage/release limits, etc)
Jordan -- Fayetteville primary flood control point
Falls -- Clayton primary FC point, but consideration of farther downstream (Goldsboro/Kinston)
Scott – Wilkesboro primary FC point
Kerr – Recently changed; weekly releases ≈ previous week’s inflows (up to 35,000 cfs)

## Slide 14: Example slides
Guide Curve (Varying)

## Slide 15: Water Quality & Low-Flow Augmentation
Releases to meet minimum downstream flow targets during low flows
Drought Contingency Plans to conserve WQ storage
Jordan (WQ 67.4% of conservation pool)
600+/-50 cfs minimum flow target at Lillington (~24 miles downstream)
Reduced target when WQ storage drops below 80% (very proactive)
Falls (WQ 41.4% of conservation pool)
Immediately below dam (100 cfs Apr-Oct; ~60 cfs Nov-Mar)
Downstream (~33 miles) at Clayton (254 cfs Apr-Oct; 184 cfs Nov-Mar)
Scott (No WQ storage)
400 cfs minimum flow target at Wilkesboro (5.5 miles downstream).
Reduced flow target when lake is more than a foot below guide curve
Kerr (No WQ storage)
Minimum energy meets downstream minimum flow requirements

## Slide 16: Water Supply
Jordan
WS storage: 45,800 AF (32.6% of conservation pool)
Estimated yield ~100 MGD
100% allocated to State of NC
95.9% of WS storage “reallocated” by State of NC
Falls
WS storage: 62,300 AF (58.6% of conservation pool) (previously 45,000 AF)
Estimated yield ~84 MGD (previously ~69 MGD)
100% allocated to City of Raleigh
Scott
WS storage: 33,000 AF (100% of conservation pool)
100% allocated jointly to City of Winston-Salem and Wilkes County
Water released as requested/needed for W-S (min releases adequate so far)
Wilkesboro/N Wilkesboro pursuing reservoir intake using County’s storage
Detailed yield analysis needed (perhaps as much as 150 MGD)

## Slide 17: Example slides
Guide Curve (Varying)

## Slide 18
Falls Storage Reallocation – Why it Worked

## Slide 19: John H Kerr Water Supply allocations
Water User | Agreement Type | Storage acre-feet (% of PP) | Date of Agreement
Virginia Beach, VA | Water Storage | 10,200 AF (1.055%) | 13-Jan-84
Henderson, NC | Water Storage | 10,292 AF (1.066%) | 17-Mar-06
VA Dept of Corrections | Water Storage | 23 AF (0.0024%) | 07-Apr-89
Mecklenburg Cogen (Dominion) | Water Storage | 600 AF (0.063%) | 20-Jun-91
TOTAL | Water Storage | 21,115 (2.186%) | 
Clarksville, VA | Grandfathered | 0.3 MGD avg | No Agreement
Burlington Industries | Grandfathered | 2.2 MGD avg | No Agreement
All Water Supply storage reallocated from Power Pool