## Slide 1
Town of Cary
Reclaimed Water
Environmental Management Commission
Water Allocation Committee Meeting January 8th, 2020
Donald Smith, Wastewater Collection System Manager
Rick Jordan, Reclaimed Supervisor
Town of Cary

## Slide 2: Today
What is Reclaimed Water?
Cary’s Story
  History/Drivers
  Use/Planning
  Challenges
  Successes
Regulatory View
  Challenges
  Opportunities

## Slide 3: Key Takeaway’s
Ideally demand is year-round & near source
Irrigation is less than originally anticipated
Regulated as “Resource” can encourage use

## Slide 4: What Exactly is Reclaimed Water?
Highly treated wastewater
(ultraviolet light and liquid chlorine)
Clear, colorless, and odorless
Not grey water
Non-potable
Potable
Reclaimed

## Slide 5: Cary’s History
Began in 2001
Service Areas
  Started with nearby residential customers & businesses
System Expansion
  Funded through Development & Capital Improvements
Regional Partnerships
  Durham County
  Wake County RTP

## Slide 6: Drivers
Reduce WWTP Nutrients Discharge
Off-set Peak Potable Demands (Irrigation)
Expand Service Portfolio for Customer Benefit
Customer Drivers Policies & Incentives

## Slide 7: How is Reclaimed Water Used in Cary?
Commercial/Industrial
Cooling Towers
Bulk Distribution
Irrigation: Commercial & Recreation
WRF Process Use
Irrigation: Residential
~60 miles of pipe
~800 Customers
  Mainly Residential Irrigation Customers
Process Use at 3 WRF

## Slide 8: Where It’s Used?
Ideally demand is year-round & near source
Irrigation is less than originally anticipated

## Slide 9: Plan Iterations
2001 – Original Policy Statement
2007 – Master Plan
2013 – Revised (MP)
2017 – Revised (MP)
2018 – Re-evaluate Services Area
2019 – Revise Service Area
Reclaimed Service Areas (July 1, 2019)

## Slide 10: Program Management
Operation & Maintenance
  Pumps & distribution piping network
  Chlorine residual
  Monthly compliance sampling
  Annual maintenance shutdown
Education & Outreach
Development Support
  Plan Review
  Inspections

## Slide 11: Operational Challenges
Seasonal Use
  Requires flushing during low-demand
Water Quality for Cooling Tower Use
  Requires supplemental WQ management
  Concentrated blow-down to sewer
System Maintenance
  Gets more complex with increasing size (tanks, chlorine boosting, more flushing)

## Slide 12: Successful Partnerships
RTP Project
  Providing RCW to a Business Campus
  Interlocal Agreement
  Regional Collaboration

## Slide 13: Is it a Waste or a Resource?
Administrative Code NCAC 15.02U interprets
reclaimed as a “waste not discharged”
Regulatory interpretation has a significant impact
Reframing it as a resources could encourage use

## Slide 14: Regulatory Challenges & Opportunities
Reporting
  Required to report any overwatering or leaks
  Handled like a sewer overflow, even on private property
Flushing
  Essentially required to blow-off to sewer system
  Consumed WRF capacity and has already been treated
Future Applications
  Indirect potable reuse

## Slide 15: Key Takeaway’s
Ideally demand is year-round & near source
Irrigation is less than originally anticipated
Regulated as “Resource” can encourage use

## Slide 16: Questions?