## Slide 1: Health-related microbial aspects of water reuse and reclaimed water quality: global, national and NC experiences and issues
Mark D. Sobsey
Research Professor
University of North Carolina
Gillings SCHOOL OF GLOBAL PUBLIC HEALTH
DEPT. OF ENVIRON. SCI. AND ENGINEERING
CHAPEL HILL, NC
EMAIL: mark_sobsey@unc.edu

## Slide 2
HEALTH-RELATED MICROBIAL ASPECTS OF RECLAIMED WATER AND WATER REUSE
Wastewater has high concentrations of pathogenic microorganisms, including bacteria, viruses and parasites
  They cause gastrointestinal and systemic illnesses in humans
    Concentrations can be up to 1012 per liter of untreated wastewater
  Removal and inactivation of pathogens is important because of increasing sensitive populations (20-25% of US population)
Reducing pathogen risks from drinking water, non-potable reclaimed water for agriculture and other uses and for discharge to recreational and drinking source waters is essential for public health.
rea

## Slide 3: Wastewater Contaminants of Health Concern
Microbial
  Bacteria: E. coli 0157, Campylobacter jejuni. Salmonella, Shigella, Legionella
  Viruses: Noroviruses, Adenoviruses, Rotaviruses, Enteroviruses, Hepatitis A Virus, Astroviruses
  Protozoan Parasites: Cryptosporidium, Giardia, Microsporidia
Chemical and Radiological
  Inorganic Chemicals
    Metals and Metalloids: Lead, Mercury, Chromium, Arsenic
    Salts: Total Dissolved Solids, Manganese salts, metal salts
    Oxyhalides: Bromate, Chlorite, Chlorate, and Perchlorate
    Nutrients: Nitrogen and Phosphorous
    Radon
  Organic Chemicals
    Often measured as TOC but now also by advance spectrometry for the many different ones
Notes: Microbes:
Common in RS and treated WW
Astrovirus – SS RNA
            Coxscakie (is an enterovirus) –more resistant to UV - also data to show coxsackie and echo are resistant to chlorine
Hep A – persistent in environment, susceptible to UV
Adeno is also very persistent and resistant
Crypto, Cl is not effective, need really high Ct values
Chemicals:
Metals - Lead, Mercury, Chromium, Arsenic: Most fall below PH guidelines – Boron can also be an issue depending on geological structure
Salts – Usually measured as TDS- salts can result in aesthetic concerns. Ca and Mg can cause damage to HH appliances(hard water), Sodium and Chloride are related to excess salinity – which can cause problems for water used for plant irrigation \
Oxyhalides- Bromate Max contaminant level is 10ug/L by EPA – perchlorate is assoc with anthropogenic activities – some states have instituted standards (MA- 2ug/L), also naturally occurs. Storage of bleach will cause chlorate and perchlorate formation
Nutrients- N and P and related constituents – especially important for irrigation and runoff
Also important for organic chemicals: industrial chemicals, pesticides, pharmaceuticals, and personal care products, food additives

## Slide 4: Fecal Microbes Causing Human Disease (Pathogens) Can Lead to Environmental Exposures Via Various Routes or Pathways
Water
Wastes
Food
Fomites
Air
Soil
Sediment
Vectors
To prevent exposures, we collect, contain and treat sewage to remove and destroy its pathogens

## Slide 5
Fecal Pathogens are Present in Different Microbe Groups
Viruses: smallest (0.02-0.3 µm diameter); simplest: nucleic acid + protein coat
Bacteria: 0.5-2.0 µm diameter; prokaryotes; cellular; simple internal organization; multiply by binary fission.
Protozoa: most >2 µm- 2 mm; eukaryotic; uni-cellular; wide range of sizes and shapes; hardy cysts, oocysts or spores; some have complex life cycles
Helminths (Worms): multicellular animals; some are human parasites; eggs are 25-150 µm; some have complex life cycles
(too big to show at scale on this graphic)
Pathogens differ in occurrence, survival, resistance to water and waste treatment, infectivity and health effects

## Slide 6: Brief (and Selective) History of Reuse
1910s- 20s: US State parks in AZ and CA begin using reuse water to supply ornamental lakes, water lawns, and to flush toilets. (Grand Canyon Nat’l Park)
1930s: San Francisco uses secondary-Rx’d. water to irrigate Golden Gate Park
1942: Baltimore, MD - Bethlehem Steel Co. uses reclaimed water for metals cooling and steel processing.
1960: City of Colorado Springs, CO - reclaimed water used for landscape irrigation of golf courses, parks, cemeteries & freeways.
1962: Los Angeles County, CA uses groundwater recharge via spreading basins.
1968:Windhoek Namibia uses advanced direct wastewater reclamation system to augment potable water supply.
1969: Wagga Wagga, Australia uses landscape irrigation of sporting fields, lawns, and fields.
1976: Orange County, CA uses groundwater recharge by direct injection.
1977: Israel uses groundwater recharge by basins for unrestricted crop irrigation
1980s: Australia uses reclaimed water for private homes. Toilets.

## Slide 7: Background on Reclaimed Water Uses
Use Category | Type of Use | Issues with Use | Benefits of Use
Landscape Irrigation | Parks, athletic fields, playgrounds, cemeteries, golf courses, school grounds, lawns | Dual distribution system Uneven seasonal demand High TDS can affect plant health | Cost savings Expand water resources Increase resiliency to climate impacts Decrease use of drinking water for non-potable uses Reduce need for chemicals Decrease wastewater discharge Environmental and ecosystem benefits
Agricultural Irrigation | Crops (food, fodder, fiber, seeds), nurseries | Use level and source distance Dual distribution system Uneven seasonal demand High TDS can affect plant health | 
Nonpotable urban uses | Toilet flushing, fire protection, chiller water, vehicle washing | Dual distribution system Building level dual plumbing Need for cross connection and contamination control | 
Groundwater Recharge | Aquifer storage and recovery, seawater intrusion control | Appropriate conditions needed High level of treatment may be required Potential for water quality degradation in subsurface | 
Potable Water Supply Augmentation | Water supply treatment and source blending | High level of treatment required Requires post-treatment storage Can be energy intensive | 
Notes: Motivation for using reclaimed water:
Limited resources, limited freshwater
Drought
Consumption
Population growth
Agriculture and industrial use
Cost savings
Uses listed on slide – want to take advantage of these uses without using DW (or water of drinkable quality)
Benefits of Reuse
1. Environmental 2. Economic
Listed in type of use section: expanding water resources WO using source water (surface water used for drinking) or DW quality water for purposes that do not require high quality water
Environmental and ecosystem benefits
Cost savings – from treating all water to DW quality: also less cost to those using the RW for irrigation (golf courses, farmers, etc), industrial purposes (cheaper on the dollar compared to DW quality water)
Reduce need for chemical fertilizers
Decreasing WW discharges, to sensitive habitats

## Slide 8: Addressing Microbial Health Risks of Water Reuse Resulting from Reclaimed Water Use and Human Exposures
Key Goal: Reduce Risks from Pathogens to Tolerable Levels
Approach: Quantitative Microbial Risk Assessment (QMRA)
  Pathogen levels in sources (e.g., sewage)
  Pathogen reductions by treatment processes (e.g., Log10 or % reductions)
  Achieve tolerable level of pathogen risk in water to which people are exposed

## Slide 9
A Watershed Scale “One Water” and “One Health” Approach is Recommended by EPA
(from the 2019 EPA National Water Reuse Action Plan Draft)
https://www.epa.gov/sites/production/files/2019-09/documents/water-reuse-2019-appendix-a.pdf
Fit for Purpose Treatment and Reuse

## Slide 10: Microbial Reduction Goals for Reuse and Potable Reuse Treatment Processes
  Goal: Reduce microbe concentrations by specific log10 values (LRVs) or percentages to achieve allowable microbe concentrations of tolerable risk from exposures
  Treatment: Often by a series of physical, chemical and biological processes (1o, 2o, 3o, 4o), with some combination of:
    Primary and secondary treatment followed by:
    Advanced membrane treatment (ultrafiltration, microfiltration, reverse osmosis) or alternative filtration processes
    Disinfection using chlorine, UV, ozone, etc.
    Combining with surface waters (protected surface water, well water, etc.) or ground water
      Further storage time and dilution for additional microbial reductions

## Slide 11: Estimated LRVs for Wastewater Treatments Processes
WHO. 2017. POTABLE REUSE. GUIDANCE FOR PRODUCING SAFE DRINKING-WATER

## Slide 13: Assessing Risk and Microbial Data Needed
Important questions:
  How is wastewater treated?
  What is the recommended type of disinfection?
  How will the reclaimed water be used?
  What are the water quality requirements?
Microbial quality usually determined by concentration of indicators, rather than pathogens of public health interest.
Preferred data needed
  Relationship between potentially regulated indicators and pathogens of public health interest.
  Or data on pathogens, preferably on infectivity (viability) to assess microbial risk related to potable or other human ingestion reuse.
Data Analysis
  QMRA – to estimate risk and compare to acceptable risk levels
    US EPA drinking water exposures: 10-4 risk of infection/person/year.
Notes: Address how microbial concerns can be identified and addressed for reclaimed water for potable reuse

## Slide 14: Important Health-Related Microorganisms
Indicators:
Always in fecal waste
High concentrations
Easy to detect and quantify
Pathogens:
Variable Presence
Low/Varying Concentrations
Difficult to detect
Bacteria
  E. coli or Fecal Coliforms (FC)
  Enterococcus spp.
Viruses
  Somatic Coliphage
  F+/male-specific Coliphage
  Total Coliphage
Protozoan Parasites
  Clostridium perfringens (all)
  Clostridium perfringens spores
Bacteria
  Salmonella spp., Campylobacter spp.
Viruses
  Adenoviruses
  Noroviruses
  Rotaviruses
Protozoan Parasites
  Cryptosporidium spp.
  Giardia spp.

## Slide 15
CURRENT WATER REUSE GUIDELINES - WHO
Key Goal: Reduce Risks from Pathogens to Tolerable Levels
World Health Organization Guidelines
  Address health risks of viruses, bacteria and parasites
    Risk based on Disability Adjusted Life Years (DALYs) as standard metric
    DALYs differ among different pathogens, based on risk of infection, illness and severity of illness. Can be “converted” to risks of infection or illness for specific pathogens
    Risks differ and vary among the pathogens
    Consider worst cases
  Wastewater Reuse in Agriculture (2006)
    Risk based on DALYs), LRVs for different crops, treatments and uses and also concentrations of FCs and helminth ova
  Potable reuse for drinking water (2017)
    LRVs of 9.5 for viruses and 8.5 for bacteria and parasites
    Also must meet all WHO Guidelines for Drinking-water Quality
    Microbial reductions to reduce risks to tolerable levels
    Can relate to needed LRVs of specific pathogens
    Standard risk metric is DALY
Notes: WHO 8.5, 9.5, 8.5

## Slide 16
CURRENT WATER REUSE GUIDELINES
INTERNATIONAL STANDARDS ORGANIZATION (ISO)
ISO has standards for viruses, bacteria and parasites in reclaimed water and biosolids of commercial, , “turnkey” sanitation systems
  LRV and microbial concentration standards for viruses, bacteria, protozoan parasites and helminths in treated liquids and solids
  Treated liquid effluent:
  Treated liquid effluent LRVs: 7 viruses, 6, bacteria, 6 protozoans, 4 helminth ova; low allowable concentrations
ISO 30500. Non-sewered sanitation systems — Prefabricated integrated treatment units — General safety and performance requirements for design and testing. 2018
Notes: WHO 8.5, 9.5, 8.5

## Slide 17
CURRENT WATER REUSE MICROBIAL GUIDELINES - USA
No uniform national standards for water reuse in the USA
  Potential via the Clean Water Act and Safe Drinking Water Act
  New efforts by EPA to update reuse guidance since 2012
State level regulations vary among different states
  California: Most stringent standards
    12-10-10 log10 reduction (LRV) rule for viruses; bacteria; and protozoa for treated wastewater intended for IPR; Texas has similar guidelines for DPR
  North Carolina: Less stringent; does not include water Rx LRVs
    2 different reclaimed water categories: types 1 and 2
    Type 1, less strict quality: <14 FC/100 mL GM; 25/100 mL max./sample
    Type 2: 6-5-4 LRVs of E. coli; coliphages; and C. perfringens
    GM/single max. concentrations: 3/25 for E. coli or FC, 5/25 for coliphages or Clostridium perfringens
    For potable use, requires reclaimed wastewater to be blended with source water at 1:3 ratio prior to conventional drinking water treatment
Notes: WHO 8.5, 9.5, 8.5

## Slide 18: NC Type 2 Reclaimed Water (NCT2RW)
Tertiary treatment then dual disinfection (UV and Chlorine)
Potable reuse: up to 20% combination of reclaimed water with surface source water + 5 days of storage
http://www.owasa.org/wastewater-management
Notes: WW Treatment generally:
Tertiary treatment (primary, secondary clarification, followed by filtration, then disinfection, x2 for Type 2
Uses for Type 1: landscaping, car washing, irrigation of food crops not directly consumed
Uses for Type 2: 20/80 combination + 5 day treatment (expansion of source water for drinking), irrigation of food crops for direct consumption
*All plants currently producing Type 1 or Type 2 use for Type 1 purposes

## Slide 19: Rationale and Need for Reuse Research in NC
Tertiary treated, dual disinfected reclaimed water has not been evaluated adequately for microbial quality in typical full-scale production scenarios.
NCT2RW has not been studied for microbial quality when blended with surface source waters and stored for 5 days.
There is a need for real-world data that documents the microbial quality, microbial reduction performance and assessment of microbial risk of NCT2RW.
Notes: Need for:
Real work, field study of microbial quality, reduction performance, and assessment of NCT2RW systems.
Pathogens and indicators in RS, RW, and SW + blending
New Information:
-Full scale production of dual disinfected RW
-Pathogen load in RS, and Surface waters (not always good data sets, will have data through time)
-Relationship between indicators and pathogens in RS, RW, and SW for methods and samples taken
-Storage of 80/20 and die-off of organisms

## Slide 20: Microbial Quality of NCT2RW for 4 NC Treatment Facilities: Study Aims
Quantify indicators and pathogens in raw sewage and reclaimed water samples
Evaluate the log10 reductions for NCT2RW producing treatment facilities
Assess pathogens risks from human exposures for use as produce irrigation water and drinking water

## Slide 21: Average Bacteria Log10 Reductions
Chart: Log10 Reductions of Bacteria from Raw Sewage to NCT2RW
| E. coli* | Enterococcus spp.* | Salmonella spp.
 | 6.3572 | 5.6203 | 4.8528
NC Reduction Target: 6 log10
= Detection Limit Value

## Slide 22: Average Virus Log10 Reductions
Chart: Log10 Reductions of Viruses from Raw Sewage to NCT2RW
| Somatic Coliphage* | F+/Male Specific Coliphage* | Total Coliphage* | Norovirus GII | Adenovirus A-F | Infectious Adenovirus
 | 4.1409 | 3.864 | 4.2071 | 3.2774 | 1.7852 | 3.2749
NC Reduction Target: 5 log10
= Detection Limit Value

## Slide 23: Average Protozoan Parasite Log10 Reductions
Chart: Log10 Reductions of Protozoan Parasites from Raw Sewage to NCT2RW
| C. perfringens (Pasteurized) | C. perfringens (Total) | Cryptosporidium spp. | Giardia spp.
 | 4.2556 | 4.4313 | 2.3462 | 2.7122
NC Reduction Target: 4 log10

## Slide 24: Key Risk Assessment Results
Potable Reuse
  Risks were not reduced below the US EPA acceptable level for drinking water exposures for pathogens.
  Adenovirus risks were the greatest in potable reuse waters.
Agricultural Reuse
  Risks were reduced below the WHO acceptable DALY level for agricultural reuse waters pathogens using subsurface drip irrigation.
  Risks from protozoan parasites, due to their presence in reclaimed waters and their survival on fruits and vegetables, were the greatest based on this analysis.
  Lower volumes of irrigation water, from subsurface drip irrigation, reduced risks.

## Slide 25: Future Needs and Directions
More health-related microbial studies of NC Type 2 reclaimed water are needed.
Existing plants producing NC type 2-like reclaimed water need to improve or optimize treatment to further reduce pathogens.
Longer term studies at more NC facilities producing NC type 2 reclaimed water are recommended, especially for plants wanting to become certified for this grade of reclaimed water.